Modern OS - Eyal’s Summary
The operating system performs two basically unrelated functions:
1. Extended Machine: Providing application programmers (and application programs) a clean, abstract set of resources instead of the messy hardware ones.
2. Resource Manager: Managing these resources
# 1. Introduction
## 1.3 Computer Hardware Review
Conceptually can be abstracted to a CPU, Memory and IO devices that are all connected by a system bus and communicate with one another over it (today there are multiple busses, multiple CPU, etc...).
### 1.3.1 Processors
The “brain” of the computer is the CPU, which fetches instructions from memory and executes them. The basic cycle of every CPU is to fetch the first instruction from memory, decode it to determine its type and operands, execute it, and then fetch, decode and execute subsequent instructions. Each CPU has a specific set of instructions that it can execute. Because accessing memory to get an instruction or data word takes longer than executing an instruction, all CPU’s contain some registers inside to hold key variables and temporary results. In addition to these general registers most computers have several special registers that are visible to the programmer:
- Program counter- contains the memory address of the next instruction to be fetched.
- Stack pointer- points to the top of the current stack in memory. Contains one frame for each procedure that has been entered but not yet exited. A frame holds those input parameters, local variables and temporary variables that are not kept in registers.
- PSW (Program Status Word)- contains the condition bits, CPU priority, mode, and other control bits.
Modern CPU’s have facilities for executing more than one instruction at the same time (with separate fetch, decode and execute units). This organization is called a pipeline. More advanced design is called a superscalar CPU where multiple execution units are present (e.g. integer arithmetic, floating point arithmetic).
Most CPUs except very simple ones, have two modes: kernel mode and user mode. In kernel mode, the CPU can execute every instruction in its instruction set and use every feature of the hardware. The OS runs in kernel mode. In contrast, user programs run in user mode, which permits only a subset of the instructions to be executed and a subset of the features to be accessed. Setting the PSW mode bit to enter kernel mode is forbidden. To obtain services from the OS, a user program must make a system call, which traps into the kernel and invokes the operating system. The TRAP instruction switches from user mode to kernel mode. When the work is completed, control is returned to the user program at the instruction following the system call.
### 1.3.2 Memory
The top layers are more costly. Top layer consists of registers internal to CPU. Typically 32x32-bits on a 32-bit CPU, generally less than 1KB. Programs must manage the registers in software. The cache memory is mostly controlled by the hardware. Main memory is divided up into cache lines, typically 64 bytes. When a program needs a memory word, and the word is located in the cache, its called a cache hit, and no memory request is sent over the bus to main memory. Some machines have two or three levels of cache. L1 cache is always inside the CPU and usually feeds decoded instructions into the CPUs execution engine. A second L1 cache can be used for heavily used data words. In addition there is usually a second cache called L2, that holds several MB of recently used memory words. Main memory is the workspace of the memory system, usually called RAM. All CPU requests that cannot be satisfied out of the cache go to main memory. In some computers the bootstrap loader used to start the computer is contained in ROM (which is nonvolatile). EEPROM, flash are also non-volatile, but can be erased and rewritten.
### 1.3.3 Disks
It takes more time to randomly access data on the magnetic disk (hard disk) than RAM, yet they are cheaper. The disk is a mechanical device, hence the time difference. At any given arm position, each of the heads can read an annular region of a metal platter called a track. All of the tracks for a given arm position form a cylinder. Each track is divided into some number of sectors. The virtual memory scheme makes it possible to run programs larger than physical memory by placing them on the disk and using main memory as a kind of cache for the most heavily executed parts. The Memory Management Unit (MMU) is responsible for remapping memory addresses on the fly to convert the address the program generated to the physical address in RAM where the word is located. In multiprogramming, performing a context switch (switching from one program to another), might require flushing all modified blocks from the cache and remapping the registers in the MMU, which might be expensive operations.
### 1.3.4 Tapes
Often used as a backup for disk storage and for holding very large data sets. Cheap, mechanical, slow, but removable so can be stored off-site to survive disasters.
### 1.3.5 IO Devices
The CPU also manages IO devices, which generally consist of two parts: a controller, and the device itself. The controller is a chip or set of chips that physically control the device. It accepts commands from the OS like read data from the device and carries them out. Because each controller is different, different software is needed to control each one. The software that talks to a controller, giving it commands and accepting responses is called a device driver. The driver must be put into the OS so it can run in kernel mode (or outside the kernel, with ability to allow a user-space driver). Three ways to relink the kernel with the new driver:
1. relink and reboot.
2. make entry in OS file then reboot.
3. accept on the fly without needing reboot.
Every controller has a small number of registers that are used to communicate with it. The collection of all the device registers forms the IO port space. On some computers the device registers are mapped into the OS address space, so they can be read and written like ordinary memory words. On other computers, the device registers are put into a special IO port space with each register having a port address. Input and output can be done by busy waiting, interrupts, Direct Memory Access (DMA). With interrupts, the driver first tells the controol what to do by writing into its device registers. Controller then starts device, reads/write what it should then signals the interrupt controller chip. If controller is prepared to accept the interrupt, it asserts a pin on the CPU chip. Then the interrupt controller puts the number of the device on the bus so CPU can read it and know which device has just finished. When CPU takes the interrupts, the device number may be used as an index into part of memory to find address of the interrupt handler for this device. This part of memory is called the interrupt vector. DMA chip can control the flow of bits between memory and some controller without constant CPU intervention. When the DMA chip is done it causes an interrupt.
### 1.3.6 Buses
The pentium system has eight buses: cache, local, memory, PCI, SCSI, USB, IDE and ISA. Each bus has different transfer rate and fucntion. The two main buses are the IBM PC ISA bus (Industry Standard Architecture) and its successor, PCI bus (Peripheral Component Interconnect). ISA runs at 8.33 MHz and can transfer 2 bytes at once, for a max speed of 16.67 MB/sec. PCI can run at 66 MHz and transfer 8 bytes at once for a data rate of 528 MB/sec. There is also PCI Express. IDE bus is for attaching peripheral devices such as disks and CDROMS. USB was invented to attach all slow IO devices (keyboard and mouse). SCSI (Small Computer System Interface) bus is a high performance bus intended for fast disks scanners etc.
The OS has to know what peripheral devices are connected and to configure them. This led Intel and Microsoft to design a PC system called plug and play. Before plug and play each IO card had a fixed interrupt request level and fixed addresses for its IO registers. If two cards used the same interrupt level a problem occurred. Plug and play has the system automatically collect information about the IO devices, centrally assign interrupt levels and IO addresses, then tell each card what its numbers are.
### 1.3.7 Booting the Computer
Every pentium contains a parentboard(aka motherboard). On the mothjerboard is a program called the system BIOS (Basic Input Output System). The BIOS contains low level IO software, including procedures to read the keyboard, write to the screen, etc. When computer is booted, BIOS is started. First checks to see how much RAM is installed, and scans ISA and PCI to see if basic devices are installed and working. Legacy devices (ones without plug and play capability), are recorded and plug and play devices are recorded. The BIOS then determines the boot device (floppy disk, CDROM, hard disk). The first sector from the boot device is read into memory and executed. This sector contains a program that nomrally examines the partition table at the end of the bott sector to determine which partitions is active. A secondary boot loader is read in from that partition. This loader reads in the operating system from the active partition and starts it. The OS then requires the BIOS to get the configuration information. For each device, it checks to see if it has the device driver. Once it has all drivers (CD ROM internet or god), the OS loads them into the kernel. Then it initializes tables, creates background processes needed and startups the login program or GUI.
## 1.5 Operating System Concepts
### 1.5.1 Processes
A process is basically a program in execution. Associated with each process is its address space, which is a list of memory locations from 0 to some maximum, which the process can read and write. The address space contains the executable program, the program’s data, and it’s stack. Also associated with each process is a set of resources, commonly including registers (including program counter and stack pointer), a list of open files, outstanding alarms, lists of related processes, and all other information needed to run the rpogram. A process is fundamentally a container that holds all the information needed to run a program. Periodically, the OS decides to stop running one process and start running another. In many OS’s, when this suspension of a process occurs, all the information about each process, other than the contents of its own address space is stored in an OS table called the process table, which is an array(or linked list) of structures, one for each process currently in existence. A suspended process consists of its address space, usually called the core image, and its process table entry.
The key process management system calls are those dealing with the creation and termination of processes. A parent process can create one or more child processes and so on. The communication between processes is called interprocess communication. Signals are the software analog of hardware interrupts and can be generated by a variety of causes in addition to timers expiring (alarms).
Each person authorized to use a system is assigned a UID by the system administrator. Every process has the UID of the person who started it, which is inherited by child processes also. One UID called the super-user (in UNIX), has special power and may violate many of the protection rules.
### 1.5.2 Address Spaces
Virtual memory allows the OS to keep part of the address space in main memory (RAM) and part on disk, rather than all in main memory. It then shuttles pieces back and forth between them as needed. This allows a process to have a larger address space than the computer has main memory (RAM). In essence, the OS creates an abstraction of an address space as the set of addresses a process may reference. The address space is decoupled from the machine’s physical memory, and may be either larger or smaller than the physical memory.
### 1.5.3 Files
Another key concept is the file system. A major function of the operating system is to hide the peculiarities of the disks and other IO devices and present the programmer with a nice, clean abstract model of device-independent files. To provide a place to keep files, most OS have the concept of a directory as a way of grouping files together. Every file within the directory hierarchy can be specified by giving its path name from the top of the directory hierarchy, the root directory. At every instant, each process has a current working directory, in which path names not beginning with a slash are looked for. Before a file can be read or written, it must be opened, at which time the permissions are checked. If access is permitted, the system returns a small integer called a file descriptor. Another important UNIX concept is the mounted file system. The mount system allows a file system to be attached to the root file system (wherever it wants), thus allowing access to content. Another UNIX concept ia the special file, which are provided in order to make IO devices look like files. This way then cay be read and written using the same system calls as are used for reading and writing files. Two kinds of special files exist: block special files and character special files.
A pipe is a sort of pseudofile that can be used to connect two processes. Thus, communication between processes in UNIX looks very much like ordinary file reads and writes. Stronger yet, the only way a process can discover that the output file it is writing on is not really a file, but a pipe is by making a special system call.
The UNIX command interpreter is called the shell.
Virtual memory gives the ability to run programs larger than the machines physical memory by moving pieces back and forth between RAM and disk.
### 1.6 System Calls
Any single CPU computer can execute only one instruction at a time. If a process is running a user program in user mode and needs a system service, such as reading or writing, it has to execute a trap instruction to transfer control to the operating system. The OS then inspects parameters to determine what the calling process wanted, then it carries out the syytem call and returns control to the instruction following the system call. Steps of ‘read’ system call:
1. Calling program first pushes the parameters onto the stack.
2. Call to the library procedure: read
3. Library procedure puts the system call number in a pre-known register by the OS.
4. Executes a trap instruction to switch from user to kernel mode and start execution at a fixed address within the kernel. The trap instruction cannot jump to an arbitrary address. Depending on architecture, it either jumps to a single fixed location, or uses field in the instruction giving the index into a table in memory containing jump addresses.
5. The kernel code that starts after trap examines the system call number and dispatches to the correct system call handler.
6. System call handler runs
7. Once work is completed, control may be returned to the user-space library procedure at the instruction following the trap instruction. This procedure then returns to the user program in the usual way procedure calls return. To finish, the program cleans the stack as it does after any procedure call.
The read system call may block, preventing the caller from continuing. In this case, the OS will look around to see if some other process can be run next.

### 1.6.1 System Calls for Process Management
Fork is the only way to create a new process in POSIX. It creates an exact duplicate of the original process including all the file descriptors, registers, etc. After the fork, the original and copy process go their separate ways. The (unchangeable) program text, is shared between parent and child. To wait for the child to finish, the parent executes a waitpid system call, which waits until any or a specific child terminates. The child process executes the user command by using the execve system call, which causes its entire core image to be replaced by the file named in its first parameter (actually system call is called exec). Processes in UNIX have their memory divided into three segments: text (program code), data (varaibles) and the stack segment. The data segment grows upward and the stack grows downward. Between them is a gap of unused address space. Stack grows into the gap automatically however expansion of the data segment is done explicitly by using a system call brk. Programmers are encouraged to use malloc.
### 1.6.2 System Calls for File Management
Open, read, write. For each file, UNIX keeps track of file mode (regular, special, directory…), size, time of last modification, etc. Programs can ask to see this via the stat system call.

# 2. Processes and Threads
The most central concept in every operating system is the process: an abstraction of a running program.
## 2.1 Processes
In any multiprogramming system, the CPU switches from process to process quickly. While strictly speaking, the CPU is running only one process at any instant in time, over the course of a seocnd it may work on several, giving the illusion of parallelism. This is sometimes known as pseudo-parallelism in contrast with true hardware parallelism of multiprocessor systems.
### 2.1.1 The Process Model
A process is just an instance of an executing program, including current values of the program counter, registers and variables. The rapid switching back and forth between processes is called multiprogramming. With the CPU switching rapidly, the rate at which a process performs its computation will not be uniform and probably not even reproducible if the same processes are run again. Thus processes must not be programmed with built-in assumptions about timing.
The difference between a process and a program is subtle but crucial. The process is an activity of some kind. It has a program, output and a state. If a program runs twice, it counts as two different processes.
### 2.1.2 Process Creation
In UNIX there is only one system call to create a new process: fork. This call creates an exact clone of the calling process. After the fork, the two processes, the parent and the child, have the same memory image, the same environment strings, and the same open files. Usually the child process then executes execve or similar to change its memory image and run a new program. After a process is created, the parent and child have their own distinct address spaces. If either process changes a word in its address space, the change is not visible to the other process.
### 2.1.3 Process Termination
Process will terminate on: normal exit, error exit (no such file exists), fatal error(divide by zero) or if killed by another process.
### 2.1.5 Process States
When a process blocks it does so because logically it cannot continue, typically because it is waiting for input that is not yet available. It is also possible for a process that is conceptually ready and able to run to be stopped because the operating system has decided to allocate the CPU to another process. A process may be in three states:
1. Running (using the CPU at that instant)
2. Ready (runnable; temporarily stopped to let another process run)
3. Blocked (unable to run until some external event happens)
In some systems, the process can execute a system call such as pause to get into a blocked state. Transitions from ready to running and opposite are caused by the process scheduler, which is part of the OS. Instead of thinking about interrupts, when using the process model we can think about user processes, disk processes, terminal processes, etc.
### 2.1.6 Implementation of Processes
To implement the process model, the OS maintains a table, called the process table, with one entry per process (entries are also known as process control blocks). This entry contains important information about the process’s state, including its program counter, stack pointer, memory allocation, status of its open files, its accounting and scheduling information, and everything else about the process that must be saved when the process is switched from running to ready or blocked state so that it can be restarted later.
Associated with each IO class is a location (typically at a fixed location near the bottom of memory) called the interrupt vector. It contains the address of the interrupt service procedure. Upon an interrupt (e.g. disk interrupt) the process’s program counter, program status word and sometimes more registers are push onto the current stack by the interrupt hardware. The computer then jumps to the address specified in the interrupt vector. The hardware’s job ends here.
If processes spend 80% of their time waiting for IO, at least 10 processes mut be in memory at once to get the CPU waste below 10%. When you realize that an interactive process waiting for a user to type something at a terminal is in IO wait state, it should be clear that IO wait times of 80% and more are not unusual.
## 2.2 Threads
In traditional OS, each process has an address space and a single thread of control. There are frequent situations in which it is desirable to have, multiple threads of control in the same address space running in quasi-parallel.